Detailed construction directions:

Print out all templates (actual size) and these directions.

Cut out all the pieces from ½ inch pine or cedar.  You can use ¾ inch material but ½ inch is strongly preferred. The use of ¾ inch material may force you to change some dimensions.

Locate the center of the opening in the front wall (3 – 5/8 inches up from the bottom edge and centered left-to-right) then drill the 7/8 inch hole.

If you plan to add a perch, drill a ¼ inch hole 2 – 1/4 inches up from the bottom edge and centered left-to-right then glue in a 2 inch long dowel.

Sand all pieces before assembly.

Cut the mitered angles on the floor and roof pieces at 9 degrees. (10 degrees is close enough.)

Position, glue, and nail the floor to the rear and front walls as shown in the original drawing.

Position, glue, and nail the floor and walls to the right wall as shown in the original drawing. Center this assembly on the wall and maintain a 3½ inch opening at the top of the walls.

Position, glue, and nail the roof pieces to the right wall as shown in the original drawing. .)

*****NOTE *****There will be a small gap between the walls and the roof when the house is finished.

Locate and drill five screw holes in the left wall and set them with a countersink. If you do not have a countersink bit, carefully use a larger bit to make the bevel. To properly locate the holes, set the right wall on the assembly then trace the walls lightly with a pencil. Locate the holes in the center of the wall thickness.

To prolong the life of the house, it is best, but not essential, to cover the roof with a roofing paper and light weight shingles.

Attach the left side with five screws to allow you to clean the house each fall.  Also, wax the screws before inserting them to make removal easier.

Add two medium sized eyehooks to the peak of the roof to facilitate hanging your birdhouse. A heavy-duty steel fishing leader works well for the hanging wire.

You can either leave the wood natural or paint it for a longer life.  However, do NOT finish the inside of the house.

Hang the house six to ten feet above the ground and in a location that is not ‘baked’ by the summer sun.

Enjoy your renters when they move in.